## Slide 1: Pediatric Neuromotor Wearable
Carl Demolder
Date 8/03/2020

## Slide 2: Outline
Project management
  Introduction
  Project requirements
Project proposal
  Block diagram
  Schematic
  PCB design
  Firmware
Schedule
  Gantt chart

## Slide 3: PROJECT MANAGEMENT

## Slide 4: Introduction
Purpose:
  Design a wearable with sensors to measure temperature, pressure, strain, and movement. This data will be wirelessly transmitted via BLE to a UI band

## Slide 5: Project requirements
Requirements:
  Design a flexible circuit to use sensors to wirelessly communicate biophysical data to a UI band
  Flexible circuit must include the following functionality:
    Wireless charging
    Battery management
    RTT data logging
    Use the nRF52832 MCU/SoC
    BLE connectivity and BLE GATT database
    Temperature sensing
    Motion sensing
    Pressure sensing
    Strain sensing

## Slide 6: Schedule overview
Electronics development
  Date range: 8/11–8/23
  Estimated hours to produce hardware: 24 hours
  Estimated hours to test/debug/qualify hardware: TBD
Firmware development
  Date range: 8/23-9/20
  Estimated hours to produce firmware: 39 hours
  Estimated hours to test/debug/qualify firmware: TBD
Any questions about the scope?
Let me know!

## Slide 7: PROJECT PROPOSAL

## Slide 8: Block diagram
BLE TX/RX
IMU
TEMPERATURE
MCU/SoC
PRESSURE
SENSOR
STRAIN
SENSOR
PHERIPHERAL SENSORS
I2C
WIRELESS
CHARGING COIL
WIRELESS CHARGING CIRCUITRY
BMS
LIPO BATTERY
POWER
POWER
POWER
POWER
RF
ANDROID PHONE**
BLE
ANALOG

## Slide 9: Electronics development: schematic
Schematic generation
  nRF52 with supporting circuitry (2 hours)
  BLE antenna and impedance matching circuit (2 hours)
  Wireless charging (5 hours)
  Lithium battery charging (2 hours)
  Biosensors: temperature, IMU (4 hours)
  Biosensors: pressure, strain (4 hours)
  Test points (1 hours)
  Project creation (3 hours)
Estimated time: 8 hours
Actual time spent: TBD
REUSING DESIGN FROM PREVIOUS PROJECTS

## Slide 10: Electronics development: PCB design
PCB design
  Major component layout (4 hours)
  BLE antenna and impedance matching circuit (3 hours)
  Wireless charging (2 hours)
  Lithium battery charging (1 hours)
  Overall board construction(1 hour)
  Biosensors: temperature, IMU, pressure, strain (3 hours)
  Test points (1 hours)
  Gerber file generation (2 hours)
  BOM generation (2 hours)
Estimated time: 16 hours
Actual time spent: TBD
REUSING LAYOUT FROM PREVIOUS PROJECTS

## Slide 11: Firmware development
Firmware
  Project and BLE stack (5 hours)
  Sensor drivers
    I2C driver (4 hours)
    Temperature driver (2 hours)
    Analog driver (3 hours)
    IMU driver (3 hours)
  RTT data logging (3 hours)
  BLE GATT database and data transfer (31 hours)
REUSING CODE FROM PREVIOUS PROJECTS

## Slide 12: SCHEDULE

## Slide 13: Schedule Gantt chart
Task | 8/2-8/9 | 8/9-8/16 | 8/16-8/23 | 8/23-8/30 | 8/30-9/6 | 9/6-9/13 | 9/13-9/20
ELECTRONICS DEVELOPMENT |  |  |  |  |  |  | 
-SCHEMATIC GENERATION |  |  |  |  |  |  | 
-PCB LAYOUT AND ROUTING |  |  |  |  |  |  | 
-HARDWARE DEBUGGING |  |  |  |  |  |  | 
FIRMWARE DEVELOPMENT |  |  |  |  |  |  | 
-PROJECT STACK ORGANIZATION |  |  |  |  |  |  | 
-SENSOR DRIVERS |  |  |  |  |  |  | 
-BLE GATT & BLE DATA TRANSFER |  |  |  |  |  |  | 
-FIRMWARE DEBUGGING |  |  |  |  |  |  | 

## Slide 14: PATH FORWARD

## Slide 15: Path forward (8/02/20 – 8/09/20)
Schematic generation
  Wheatstone bridge
PCB layout

## Slide 16: APPENDIX

## Slide 17: Component selection: MCU/BLE
MCU/BLE: nRF52832
  6 pin, 2.00 mm x 2.00 mm, WSON-6
  ±0.1°C from -20°C to +50°C
  2.4 GHz BLE
  Power = 4 dBm
  Sensitivity = -96 dBm
  RAM = 64 kB, flash = 512 kB
  Serial interfaces: I2C, UART, SPI
  Supply voltage: 1.7V ~ 3.6V
  $5.46 [X1], 1490-1067-1-ND, LINK
nRF52832

## Slide 18: Component selection: clocks
HF clock: US3200005Z
  4 pin, 1.60 mm x 1.20 mm, 4-SMD
  32.00 MHz, 8 pF, ±10 ppm
  $1.45 [X1], US3200005ZCT-ND, LINK
LF clock: ECX-1210
  1210 package, 1.20 mm x 1.00 mm, 2-SMD
  32.7680 kHz, 9 pF, ±20 ppm
  $1.52 [X1], XC2283CT-ND, LINK
ECX-1210
US3200005Z

## Slide 19: Component selection: Bio-sensors
Temperature: TI TMP117
  6 pin, 2.00 mm x 2.00 mm, WSON-6
  ±0.1°C from -20°C to +50°C
  16-bit resolution: 0.0078 °C, I2C
  $8.02 [X1], 296-51834-1-ND, LINK
IMU: TI BQ27621-G1
  14 pin, 2.5 mm x 3.0 mm, 14-LGA
  I2C communication
  9-axis, 16-bit resolution
  Full operation mode = 925 uA
  $4.98 [X1], 828-1057-1-ND, LINK
BMI160
TMP117

## Slide 20: Component selection: Bio-sensors
Pressure & Strain: LMV981
  6 pin, 1.5 mm x 1.3 mm, 6-DSPGA
  Differential Amplifier, I2C
  $1.63 [X2], LMV981, LINK
LMV981

## Slide 21: Component selection: wireless charging
Wireless charging IC: TI BQ51003
  28 pin, 1.90 mm x 3.00 mm
  QI v1.2 communication protocol
  93% AC-DC efficiency
  $3.00 [X1], 296-39952-1-ND, LINK
LiPo battery charger IC: TI BQ25100
  6 pin, 1.6 mm x 0.90 mm, 4.2V 1 cell
  1% Charge voltage accuracy
  10 mA to 250 mA charging current
  $2.24 [X1], 296-38373-1-ND, LINK
BQ25100
BQ51003

## Slide 22: Component selection: power circuit
Reed Switch: ABLIC S-5712A
  4 pin, 1.90 mm x 3.00 mm, SNT-4A
  Non-contact ‘power switch’
  High accuracy hall effect switch IC
  $1.07 [X1], 1662-1617-1-ND, LINK
Linear Regulator: Analog Devices ADP172
  4 pin, 0.95 mm x 1.03 mm, 4-WLCSP
  0.1V dropout voltage
  300 mA max current
  $1.09 [X1], ADP172ACBZ-3.0-R7CT-ND, LINK
ADP172
S-5712A

## Slide 23: Component selection: power circuit
Charging coil: Wurth 760308101219
  1 coil, 1 layer, D=15 mm, H=0.6 mm
  11.8 uH, 750 mΩ, t = ±10%
  $7.43 [X1], 732-9675-ND, LINK
760308101219